## Slide 1
Post-earthquake Building Usability Assessment:
Level 1: Rapid Evaluation
Jitendra Bothara

## Slide 2
Levels of Evaluation
  Level 1: Rapid Evaluation
  Level 2: Detailed evaluation
  Level 3: Detailed Engineering
Rapid Evaluation
  Objective of Evaluation
  Goals
  Building categorisation
  Steps
Content

## Slide 3
Triaging of buildings – identify which buildings are usable,
A safety evaluation of current state of buildings with anticipation of aftershocks sequence, to identify whether the building is safe for entry or occupancy.
It is not future proofing of buildings. It should not consider issues of code compliance.
Level 1: Rapid Evaluation

## Slide 4
  Qualitative
  completed immediately after an earthquake
  establishing quantum of damage
  external only
  less than 10-20 minutes
  categorising buildings into Inspected/ Limited Entry/ Unsafe,
  recommending barriers and/or no-go zones.
Level 1: Rapid Evaluation

## Slide 5
Identify which buildings are usable.
minimising displacement of people.
  Send people back to their home, if that is safe to do – normalcy in life
  assessing the need for temporary works such as shoring, temporary securing/ removal of unstable elements and making safe
  saving property from unnecessary demolition conserving heritage fabric
Objective

## Slide 6
Safe use of streets adjacent to damaged buildings
  safe occupation of buildings for: continued use, especially emergency facilities
minimising economic impact for the owners and community
minimising impact on commercial activities
The goal is to minimise risk, but not to
  imposing unwarranted hardship on owners and occupants of damaged buildings
Objective………

## Slide 7
GREEN – Does not mean safe, it only means the building is occupiable in given condition,
YELLOW:
RED: Does not mean the building has to be demolished
The goal is to understanding the implications of the damages
Interpretation

## Slide 8
Damage Categorisation
Damage Intensity | Risk Profile | Posting | Usability Category | Details
Light | Low | Inspected (Green) | Occupiable | Occupiable
Moderate | Moderate | Restricted, Limited entry at owner’s risk (Yellow) | Use restricted to parts of building only | Prohibit entry into certain rooms/ areas or whole building because of falling hazards that do not threaten the rest of the building,
 |  |  | No public entry except on short term essential business to parts or all of the building for emergency purpose | Removal of essential business or legal records, removal of valuables only, removal of property
Heavy | High | Unsafe, entry prohibited, (Red) | Entry prohibited: Damage to external factors pose a significant hazard | Geotechnical, adjoining buildings, gas/ electricity,
 |  |  | Entry prohibited: Structural factors | Leaning, total/ partial collapse of walls, severe damage to structural columns, load paths lost, capacities severely compromised

## Slide 9
Rapid Assessment Process
Building identified for assessment
Assessment by visual examination of the exterior and interior
Confirm and record the identity of the building
Assess/ Record/ Decide
Occupiable
Restricted access
Entry Prohibited

## Slide 10
Life-safety threat
Threat of overall or partial collapse due to loss of strength, stability, or stiffness of the structural system
Building or storey leaning
Collapse, partial collapse or off foundation
Structural damage to vertical load system
  Out-of-plumb walls/ columns, beam-column
Structural damage to lateral load system
  Hinging of columns/ beams,
What we are looking for?

## Slide 11
Falling hazards – parapets, canopies, gable walls, broken windows
Threat posed by damage to adjacent structures or land
Ground slope movement
  Look for ground displacement
  Foundation damage
Other hazards such as gas, power cables, other hazardous materials
What we are looking for?

## Slide 12
Inspect the entire building from outside,
Examine the ground in the general area of the building for fissures, land or rock slide, slope movement,
Complete the Rapid Evaluation Form/ App
Provide brief notes to the house owners, if that helps to reduce risk – talk to them
Please be aware: You are the most knowledge person for the house owner so provide him accurate information only.
Inspection Procedure

## Slide 13
Damage Categorisation
Damage Intensity | Risk Profile | Posting | Usability Category | Details
Light | Low | Inspected (Green) | Occupiable (no immediate further work required) | No apparent hazard observed, although repairs may be required, original vertical/ lateral load capacity has not significantly reduced, minor non-structural damage,
Moderate | Moderate | Restricted, Limited entry at owner’s risk (Yellow) | Use restricted to parts of building only | Local damages, falling hazard, structure intact and its capacity not compromised
 |  |  | No public entry except on short term essential business to parts or al of the building for emergency purpose | Vertical load carrying capacity significantly not compromised , lateral load capacity significantly reduced, high risk from aftershocks, emergency support may be required, no entry to public
Heavy | High | Unsafe, entry prohibited, (Red) | R1. Significant damage: repairs, strengthening possible | Extreme hazard, may collapse from an aftershock. Significant loss of vertical load capacity, severe loss of lateral load capacity, partial failure could have occurred, however load paths still available, building surrounding may need cordoning,
 |  |  | R2. Severe damage: demolition likely | Load paths lost, capacities severely compromised

## Slide 14
Damage Categorisation
Posting | Usability Category | Details
Inspected (Green) | Occupiable | Occupiable
Restricted, Limited entry at owner’s risk (Yellow) | Use restricted to parts of building only | Prohibit entry into certain rooms/ areas because of falling hazards that do not threaten the rest of the building,
 | No public entry except on short term essential business to parts or all of the building for emergency purpose | Removal of essential business or legal records, removal of valuables only, removal of property
Unsafe, entry prohibited, (Red) | Entry prohibited: Damage to external factors pose a significant hazard | Neighbouring building or its components in danger of collapse, risk of land slide/ rock fall, significant crack(s) in the ground to or under building
 | Entry prohibited: Structural factors | Leaning, total/ partial collapse of walls, severe damage to structural columns and beams/ walls, load paths lost, capacities severely compromised

## Slide 15
Post-earthquake Usability Evaluation of a building should be based on overall safety performance of the building rather than performance of a single or a few components.

## Slide 16
Advisory
Counselling
Our Role

## Slide 17
Team must have at least two members
Why
  Safety
  Discussion/ Peer review
Team Building

## Slide 18
PPE
Official identification/authorisation to enter properties
Street maps, aerial photographs and building specific information etc.,
Assessment forms/ App,
Essential Items

## Slide 19
Briefing Sheets:
  outline procedures,
  reporting requirement,
  contact points (etc.),
Office supplies
  Clip boards,
  Pens and pencils,
  Spare batteries including means of re-charging electronic equipment,
Carry bag,
Camera
Essential Items……

## Slide 20
ANY QUESTION?